Artic

Artic

FORM – CRASH TESTS

Rev. 9/19/19

VEHICLE INFORMATION / TEST SPECIFICATIONS

FMVSS No. 301

Vehicle Model Year and Make:

Vehicle Model and Body Style:

SEAT MID FORE - AFT POSITION, HEIGHT, AND CUSHION ANGLE

The rearmost position is determined by using all the seat controls that have any affect on the fore-aft movement of the seat to move the seat cushion to the rearmost position. The forward most position is determined by using all the seat controls that have any affect on the fore-aft movement of the seat to move the seat cushion to the foremost position. The mid position is then determined from these two extremes. (Refer to the diagrams below to assist in attaining proper measurements specific to seat travel area type. A = Complete range of travel and B = A/2.) While maintaining the mid position, the seat is moved to its lowest position.

SEAT TRAVEL TYPE 1	SEAT TRAVEL TYPE 2

LEFT SIDE VIEW

SEAT CUSHION

SEAT TRAVEL

B le

A

LEFT SIDE VIEW

SEAT CUSHION

B	le

A

SEAT TRAVEL

Driver’s Seat

Manual seat track adjusters:  Total number of detents:  	  Mid Fore-Aft Seat detent (with the forward-most detent defined as 0):

Power seat track adjusters: Complete range of travel (A): 		mm Distance from the forward-most position to the test position (B): 	mm

Seat cushion angle: If the seat cushion angle is adjustable while maintaining the mid fore-aft seat track, describe the angle used during certification testing, how to measure it, and any reference points. (Include photographs.)

Seat cushion height: If the seat height is adjustable at the mid fore-aft seat track position and can be adjusted so that the seat cushion angle can be at the angle used in the certification test, describe the height used during certification testing, how to measure it and any reference points. (Include photographs.)

Provide any other instructions for positioning the seat at the center of fore and aft travel, with the certification seat cushion angle, at the lowest height:

Front Outboard Passenger seat:

Manual seat track adjusters:  Total number of detents:  	  Mid Fore-Aft Seat detent (with the forward-most detent defined as 0):

Power seat track adjusters: Complete range of travel (A): 		mm Distance from the forward-most position to the test position (B): 	mm

Seat cushion angle: If the seat cushion angle is adjustable while maintaining the mid fore-aft seat track, describe the angle used during certification testing, how to measure it, and any reference points. (Include photographs.)

Seat cushion height: If the seat height is adjustable at the mid fore-aft seat track position and can be adjusted so that the seat cushion angle can be at the angle used in the certification test, describe the height used during certification testing, how to measure it, and any reference points. (Include photographs.)

Provide any other instructions for positioning the seat at the center of fore-aft travel, with the certification seat cushion angle, and at the lowest height:

Rear Seats (side impact ONLY)

Manual seat track adjusters:  Total number of detents:  	  Mid Fore-Aft Seat detent (with the forward-most detent defined as 0):

Power seat track adjusters: Complete range of travel (A): 		mm Distance from the forward-most position to the test position (B): 	mm

Seat cushion angle: If the seat cushion angle is adjustable while maintaining the mid fore-aft seat track, describe the angle used during certification testing, how to measure it, and any reference points. (Include photographs.)

Seat cushion height: If the seat height is adjustable at the mid fore-aft seat track position and can be adjusted so that the seat cushion angle can be at the angle used in the certification test, describe the height used during certification testing, how to measure it, and any reference points. (Include photographs.)

Provide any other instructions for positioning the seat at the center of fore-aft travel, with the certification seat cushion angle, and at the lowest height:

50th MALE NOMINAL DESIGN RIDING POSITION SEAT BACK ANGLE

Driver’s Seat

With the seat in the mid fore-aft seat

UPRIGHT POSITION

- ANGLE

+ ANGLE

track position, what is the angle of the seat back when it is in the forward-most locked position?

With the seat in the mid fore-aft seat track position, what is the angle of the driver’s seat back when it is in the

FORWARD-MOST LOCKED POSITION

SEAT CUSHION

LEFT SIDE VIEW

TEST POSITION

INCLINOMETER

ADJUSTER

nominal design riding position (FMVSS 208 S8.1.3)?

Is the seat back angle measured with the dummy in the seat?	Yes 	No

Describe any references used for measuring the seat back angle, e.g., door sill. (Include photographs.)

Front Outboard Passenger Seat

With the seat in the mid fore-aft seat track position, what is the angle of the seat back when it is in the forward-most locked position?

With the seat in the mid fore-aft seat track position, what is the angle of the driver’s seat back when it is in the nominal design riding position (FMVSS 208 S8.1.3)?

Is the seat back angle measured with the dummy in the seat?	Yes 	_	No

Describe any references used for measuring the seat back angle, e.g., door sill. (Include photographs.)

2nd Row Seat

With the seat in the mid fore-aft seat track position, what is the angle of the seat back when it is in the forward-most locked position?

With the seat in the mid fore-aft seat track position, what is the angle of the driver’s seat back when it is in the nominal design riding position?

Is the seat back angle measured with the dummy in the seat? Yes 	No

Describe any references used for measuring the seat back angle, e.g., door sill. (Include photographs.)

3rd Row Seat

With the seat in the mid fore-aft seat track position, what is the angle of the seat back when it is in the forward-most locked position?

With the seat in the mid fore-aft seat track position, what is the angle of the driver’s seat back when it is in the nominal design riding position?

Is the seat back angle measured with the dummy in the seat? Yes 	No

Describe any references used for measuring the seat back angle, e.g., door sill. (Include photographs.)

ADJUSTABLE D-RING SEAT BELT ANCHORAGE POSITION

50th Male nominal design position

Range of travel: 	mm

Distance from the upper-most position to the nominal design position:

mm

If detents are available, total number of detents:  	                             Nominal design position detent (with the upper-most detent defined as 0):

5th Female nominal design position

Range of travel: 	mm

Distance from the upper-most position to the nominal design position:

mm

If detents are available, total number of detents:  	                             Nominal design position detent (with the upper-most detent defined as 0):

STEERING COLUMN AND WHEEL ADJUSTMENTS

If the steering wheel and /or steering column adjustments are available, provide any specific procedures used to determine the geometric center of the locus the steering wheel hub describes when it is moved through its full range of driving positions.

STEERING COLUMN ASSEMBLY

3

2

1

LEFT SIDE VIEW

Angle of the steering wheel with respect to vertical when the steering wheel hub is positioned at the geometric center of the locus it describes when it is moved through its full range of driving positions: 	degrees

If detents are also available, please provide the following: Total number of detents:

Test detent when steering wheel hub is positioned at the geometric center of the locus it describes when it is moved through its full range of driving positions (with the upper-most detent defined as 0):

DUMMY MEASUREMENTS FOR THE 50TH MALE AND 5TH FEMALE

See the attached instructions and diagram and provide measurements for the following seat configurations

Driver (Manual Seat) Driver (Power Seat) Passenger (Manual Seat) Passenger (Power Seat)

Second Row Occupant (Side impacts only)

FUEL TANK CAPACITY DATA

(“Capacity” is define in Part 571.3 as the fuel tanks unusable capacity plus the usable capacity. The term does not include the vapor volume of the tank nor the volume of the fuel tank filler neck.)

Fuel Tank Capacity used when certification testing to requirements of FMVSS No. 301= 	gallons.

|  | (gallons) |
| --- | --- |
| Usable Capacity |  |
| Unusable Capacity |  |
| Total Capacity |  |

Standard Fuel Tank

VEHICLE FUEL TANK ASSEMBLY

VAPOR VOLUME

FUEL LINE

USABLE CAPACITY

FILLER PIPE VOLUME

FILLER CAP

Optional Fuel Tanks

|  | (gallons) |
| --- | --- |
| Usable Capacity |  |
| Unusable Capacity |  |
| Total Capacity |  |

Operational instructions:

USABLE CAPACITY

UNUSABLE CAPACITY

Suggested methods for draining:

Is vehicle equipped with electric fuel pump?	Yes 		No

If YES, does pump normally operate when vehicle's electrical system is activated?

Yes 		No

If YES, explain the vehicle operating conditions under which the fuel pump will pump fuel:

FUEL TANK LOCATION

Provide drawing (or description) that shows the undercarriage view and/or location.

FRONT OUTBOARD PASSENGER SEAT

Is the air bag activated when a 5th percentile female or 50th percentile male dummy is in the seat?

YES	 	NO	(System bypass information needed)

SPECIAL INSTRUCTIONS

Please make note of any special instructions that you would like NHTSA to consider or be made aware of for the tested vehicle (ex. towing setup, refrain from using seat belt load cells, etc.):

9