## Slide 1: INTRODUCTION/HISTORY
Chapter 1

## Slide 2: MODULE CONTENT
Chapter 1: Introduction and History
Chapter 2: Scientific Principles
Chapter 3: Function
Chapter 4: R.A.D.A.R. Effects
Chapter 5: Set up
Chapter 6: Testing
Chapter 7: Operate
Chapter 8: Legal Considerations

## Slide 3: R.A.D.A.R.
dio
etection
nd
anging

## Slide 4: HISTORY OF R.A.D.A.R.
1972
1947
1946
1939
1935
1886
1842
Christian Johann Doppler discovers the “Doppler Principle”
Heinrich Hertz is the first to observe radio waves
R.A.D.A.R. is developed for military use in detecting aircraft
First ground R.A.D.A.R. station becomes operational
Military lifts restrictions on R.A.D.A.R. following World War II and attention turns to development for civilian applications
Use of R.A.D.A.R. by law enforcement begins
R.A.D.A.R. tech advances allowing use of speed-measuring devices in moving patrol vehicles

## Slide 5: SCIENTIFIC PRINCIPLES
Chapter 2

## Slide 6: DOPPLER PRINCIPLE
Based upon sound waves
Later determined to apply to other types of waves
  Radio
  Light
“The frequency of a wave is relative to the motion between the source and the observer.”

## Slide 7
Higher Frequency
Lower Frequency

## Slide 8: RELATIVE MOTION
Stationary
Objects Moving Away
Objects Moving Towards
Notes: Needs updated graphics

## Slide 9: RELATIVE MOTION
R.A.D.A.R.s can determine
  Target presence
  Direction
  Speed
  Range
Police traffic R.A.D.A.R. devices computes speed from RELATIVE MOTION ONLY

## Slide 10: R.A.D.A.R. USES RADIO WAVES
Doppler principle (based on sound) also applies to:
Light Waves
Radio Waves

## Slide 11: WAVE AND WAVELENGTH
A
Valley
A to B = WAVELENGTH
One Wave
Peak
B

## Slide 12: TYPES OF WAVES & THEIR MEDIUMS
Ripple in pond, ocean waves: Water
Sound waves, blast waves: Air
  Seismic waves (sound waves that travel through rock)
Electromagnetic waves: Space

## Slide 13: THE ELECTROMAGNETIC SPECTRUM
L.I.D.A.R. (330 THz)
X Band R.A.D.A.R. K Band R.A.D.A.R. Ka Band R.A.D.A.R.
(10.525 GHz) (24.15 GHz) (33.4 GHz-36 GHz)
FREQUENCY INCREASE (CYCLES PER SECOND)
WAVELENGTHS DECREASE

## Slide 14: WAVELENGTH
AM Radio
950 feet long
Police Radio
6 feet long
X-Band R.A.D.A.R.
1.1 inch
K-Band R.A.D.A.R.
0.49 inch
Ka-Band R.A.D.A.R.
0.34 inch
Notes: Needs updated graphics

## Slide 15: TARGET COMPOSITION - SIGNAL PROPERTY
Reflected
Metal
Concrete
Refracted
Glass
Absorbed
Grass
Earth
Sand
Notes: Needs updated graphics

## Slide 16: MAIN LOBE
Contains Approximately 85%
of the Signal’s Power
Side Lobes

## Slide 17
250’
500’
750’
1000’
9 degrees of angle
12 degrees of angle
18 degrees of angle
39’
79’
118’
157’
53’
105’
158’
210’
79’
158’
238’
317’
Typical “Ka” Band Beamwidths
Typical “K” Band Beamwidths
Typical “X” Band Beamwidths
Notes: Needs updated graphics

## Slide 18: FUNCTION
Chapter 3

## Slide 19: DEVICES & MODES OF OPERATION
Stationary
Moving Opposite
Moving Same

## Slide 20: STATIONARY OBJECT REFLECTS AT SAME FREQUENCY
Transmitted Frequency
Reflected Frequency
Fixed Object
Notes: Needs updated graphics

## Slide 21: INCOMING OBJECT REFLECTS AT HIGHER FREQUENCY
Transmitted Frequency
Reflected Frequency
Object Moving Toward
Notes: Needs updated graphics

## Slide 22: RETREATING OBJECT REFLECTS AT LOWER FREQUENCY
Object Moving Away
Transmitter
Transmitted Frequency
Reflected Frequency
Object Moving Away
Notes: Needs updated graphics

## Slide 23
Vehicle Speed M.P.H. | Frequency Shift (waves per second) |  | 
 | “X” Band | “K” Band | “Ka” Band
1 | 31.4 | 72 | 99.6-107.3
5 | 157 | 360 | 498-536.5
10 | 314 | 720 | 996-1073
15 | 471 | 1080 | 1494-1609.5
25 | 785 | 1800 | 2490-2682.5
40 | 1256 | 2880 | 3984-4292
55 | 1727 | 3960 | 5478-5901.5
70 | 2198 | 5040 | 6972-7511
80 | 2512 | 5760 | 7968-8584
100 | 3140 | 7200 | 9960-10730

## Slide 24: R.A.D.A.R. “DECISION MAKING”

## Slide 25: R.A.D.A.R. “DECISION MAKING”
Notes: Needs updated graphics

## Slide 26: R.A.D.A.R. TRACKING HISTORY
VISUAL OBSERVATION
  Target Identification
  Speed Estimation
  Target Range
  Check Environment
AUDIO CONFIRMATION
  Pitch
  Clarity
UNIT CONFIRMATION
  Consistent with visual estimate
  Steady reading

## Slide 27: MOVING R.A.D.A.R.
Basic operation similar to stationary R.A.D.A.R.
R.A.D.A.R. is in motion
Antenna transmits a single beam

## Slide 28: PATROL SPEED
Doppler frequency determined by the R.A.D.A.R. beam reflected from roadway
Normally, directly in front of the R.A.D.A.R. device

## Slide 29: LOW DOPPLER
The term given to the frequency shift reflected from the roadway or environment
Must be established by the R.A.D.A.R. device prior to determine the target vehicle’s speed

## Slide 30: HIGH DOPPLER
The term given to the higher Doppler frequency reflected from the oncoming vehicle
Target vehicle speed can be calculated only if a low Doppler has been established

## Slide 31: MOVING R.A.D.A.R. BLOCK DIAGRAM
High Doppler Filter
Antenna
TS = CS - PS
TS =
CS =
PS =
R.A.D.A.R. Unit Display
Low Doppler Filter
Notes: Needs updated graphics

## Slide 32: CLOSING SPEED
The speed of the relative motion between the target vehicle and the patrol vehicle as the vehicles approach each other

## Slide 33: TARGET SPEED OPPOSITE DIRECTION
Front Antenna
Transmitter
Notes: Needs updated graphics

## Slide 34: SEPARATION SPEED
The speed of the relative motion between the target vehicle and the patrol vehicle as the vehicles move away from each other in an opposite direction

## Slide 35: TARGET SPEED OPPOSITE DIRECTION
Rear Antenna
Transmitter
Notes: Needs updated graphics

## Slide 36: MOVING R.A.D.A.R. TRACKING HISTORY (OPPOSITE LANE)
VISUAL OBSERVATION
  Target Identification Speed Estimation Target Range Check Environment
AUDIO CONFIRMATION
  Audio “Doppler Tone” is consistent with estimated speed (pitch, clarity)
UNIT CONFIRMATION
  Displayed target speed is consistent with estimated speed and audio, steady reading
COMPARE PATROL SPEED DISPLAY WITH THE SPEEDOMETER READING

## Slide 37: SAME DIRECTION MOVING R.A.D.A.R.
Target Speed = Patrol Speed + Separation Speed
TS = 55 mph + 20 mph
TS = 75 mph
Target Speed = Patrol Speed - Closing Speed
TS = 85 mph - 15 mph
TS = 70 mph

## Slide 38: CORRECT MODE SETTING
Target Speed = Patrol Speed + Separation Speed = mph
TS = 50 mph + 20 mph = 70
TS = 51 mph + 19 mph = 70
TS = 52 mph + 18 mph = 70
TS = 53 mph + 17 mph = 70
TS = 54 mph + 16 mph = 70
TS = 55 mph + 15 mph = 70

## Slide 39: INCORRECT MODE SETTING
Target Speed = Patrol Speed + Separation Speed = mph
TS = 50 mph + 20 mph = 70
TS = 51 mph + 21 mph = 72
TS = 52 mph + 22 mph = 74
TS = 53 mph + 23 mph = 76
TS = 54 mph + 24 mph = 78
TS = 55 mph + 25 mph = 80

## Slide 40: Moving R.A.D.A.R. Tracking History (Same Lane)
VISUAL OBSERVATION
AUDIO CONFIRMATION
UNIT CONFIRMATION
SPEED DISCRIMINATION
COMPARE PATROL SPEED DISPLAY WITH THE SPEEDOMETER READING
  Target Identification Speed Estimation Target Range Check Environment
  Audio “Doppler Tone” is consistent with estimated speed (pitch, clarity)
  Displayed target speed is consistent with estimated speed and audio, steady reading
  Patrol speed should be varied to determine proper mode setting

## Slide 41: R.A.D.A.R. EFFECTS
Chapter 4

## Slide 42: R.A.D.A.R. EFFECTS
Notes: Needs updated graphics

## Slide 44: ANGLE EFFECT AS VEHICLE APPROACHES
Target
Patrol
Traffic flow
(Two-Lane Highway)

## Slide 45: TRUE SPEED AS AFFECTED BY THE COSINE EFFECT
Angle Degrees | 30 mph | 40 mph | 50 mph | 55 mph | 60 mph | 70 mph
0 | 30 | 40 | 50 | 55 | 60 | 70
1 | 29.99 | 39.99 | 49.99 | 54.99 | 59.99 | 69.99
3 | 29.96 | 39.94 | 49.93 | 54.92 | 59.92 | 69.90
5 | 29.89 | 39.85 | 49.81 | 54.79 | 59.77 | 69.73
10 | 29.54 | 39.39 | 49.24 | 54.16 | 59.09 | 68.94
15 | 28.98 | 38.64 | 48.30 | 53.12 | 57.94 | 67.61
20 | 28.19 | 37.59 | 46.99 | 51.68 | 56.38 | 65.78
30 | 25.98 | 34.64 | 43.30 | 47.63 | 51.96 | 60.62
45 | 21.21 | 28.28 | 35.36 | 38.89 | 42.43 | 49.50
60 | 15.00 | 20.00 | 25.00 | 27.50 | 30.00 | 35.00
90 | 00.00 | 00.00 | 00.00 | 00.00 | 00.00 | 00.00

## Slide 46: LOW DOPPLER COSINE
Usually result of improper antenna aim
Antenna must be aimed STRAIGHT AHEAD
The cosine effect may, on occasion, decrease the perceived patrol speed and thereby increase the perceived target speed

## Slide 47: MOVING EXAMPLE 1
Actual Speeds
Cosine Effect
CS - PS = TS
110 - 50 = 60
100 - 50 = 50
Patrol
Target 60 mph
10 mph too LOW

## Slide 48: MOVING EXAMPLE 2
Actual Speeds
Cosine Effect
CS - PS = TS
110 - 50 = 60
100 - 50 = 50
Patrol
10 mph too LOW
Target 60 mph

## Slide 49: MOVING EXAMPLE 3
Actual Speeds
Cosine Effect
CS - PS = TS
110 - 50 = 60
110 - 40 = 70
Patrol
Target 60 mph
Fence
Large Building – etc.
10 mph too HIGH
Notes: Needs updated graphics

## Slide 50: MISALIGNMENT EFFECT ON PATROL SPEED DISPLAY AT 50 MPH
zero mph
90o
25 mph
60o
50 mph Patrol
43.3 mph
30o
8o
49.5 mph
0o
50 mph
Notes: Needs updated graphics

## Slide 51: SCANNING (FEEDBACK) EFFECT
POSSIBLE WITH TWO-PIECE R.A.D.A.R. ONLY
Caused by aiming antenna at the counting unit
Easy to detect
To Avoid
  Use proper antenna mounting
  Listen to the Audio Doppler
  Use tracking history

## Slide 52: PANNING
R.A.D.A.R. detects motion
Panning causes R.A.D.A.R. to interpret its own motion as speed
Possible with two-piece R.A.D.A.R. if antenna is hand-held
To Avoid
  Use mounting devices provided
  Disregard readings while antenna is in motion
  Use tracking history

## Slide 53: BATCHING
MOVING MODE ONLY
Cause by rapid acceleration or deceleration with failure of R.A.D.A.R. to update patrol speed
Difficult to demonstrate in newer units
To Avoid
  Disregard reading while rapid acceleration or deceleration
  Use tracking history

## Slide 54: SHADOWING
MOVING MODE ONLY
Caused by overtaking large vehicle
Low Doppler reestablished from overtaking speed
To Avoid
  Compare patrol speed with speedometer
  Use tracking history

## Slide 55: SHADOWING EXAMPLE
Actual Speeds
Shadowing Effect
CS - PS = TS
110 - 50 = 60
110 - 15 = 95
Patrol
Target 60 mph
Large Vehicle 35 mph
35 mph too HIGH

## Slide 56: OWN SPEED CAPTURE
MOVING MODE ONLY
Same speed reading in both patrol and target displays
Result of “triple Doppler shift”
To Avoid
  Decelerate patrol vehicle & check display for reading
  Use tracking history

## Slide 57: EXTERNAL MECHANICAL INTERFERENCE
Remember that R.A.D.A.R. detects MOTION, not DIRECTION
Any large moving object in R.A.D.A.R. beam may cause a reading
To Avoid
  Check operating environment
  Develop a valid tracking history

## Slide 58: PULSATING SIGNAL AMPLITUDE EFFECT
MOVING MODE ONLY
R.A.D.A.R. beam is reflected from an irregular surface with constant pattern
To Avoid
  Observe environment
  Use Audio Doppler
  Use tracking history

## Slide 59: RADIO FREQUENCY INTERFERENCE (R.F.I.)
ELECTRICAL SOURCES
Possible source of interference
Usually accompanied by loud audio noise
The higher the voltage the greater possibility of interference
To Avoid
  Choose location carefully
  Check location with Audio Doppler
  Use tracking history

## Slide 60: POWER SURGES
Was a problem with older units
Units buffer power on power-up
HOLD function will not cause power surge
To Avoid
  Allow R.A.D.A.R. to stabilize when turned on
  Do not use power plug as HOLD function
  Use tracking history

## Slide 61: R.F.I. THROUGH POWER, ANTENNA LEADS
Power lead capable of causing interference
To Avoid
  Use well shielded power and antenna leads
  Do not intertwine power and antenna leads
  Use tracking history

## Slide 62: INTERFERENCE INSIDE PATROL VEHICLE
Many potential sources of interference
Both electronic and mechanical
To Avoid
  Check for interference with R.A.D.A.R.
  Listen to Doppler Audio carefully
  Use tracking history

## Slide 63: RANDOM R.F.I.
Radio signals generated by some electronic device
Usually identifiable
To Avoid
  Check Audio Doppler carefully
  Develop a valid tracking history

## Slide 64: R.F.I. FROM POLICE AND BUSINESS RADIOS
May cause interference
To Avoid
  Don’t transmit while using R.A.D.A.R.
  Disregard if other transmitter is nearby
  Use tracking history

## Slide 65: R.F.I. FROM LIGHTING DEVICES
Mercury vapor, fluorescent, neon lighting may cause R.F.I.
To Avoid
  Choose R.A.D.A.R. location carefully
  Listen to Doppler Audio during set-up
  Use tracking history

## Slide 66: HARMONIC SIGNAL INTERFERENCE
Harmonic is a multiple of a base frequency
Some electrical devices may produce interference
To Avoid
  Use the Doppler Audio to identify harmonics
  Use tracking history

## Slide 67: WINDSHIELD OBSTRUCTIONS
Remember reflection, refraction, absorption
May result in reduced range
Will not affect accuracy
To Avoid
  Keep windshield clean, free of obstructions
  Aim antenna properly
  Use tracking history

## Slide 68: DENTED ANTENNA HORN
WILL NOT affect accuracy of R.A.D.A.R.
WILL affect range, beam shape
To Avoid
  Prevent abuse of unit
  Use tracking history

## Slide 69: ANTENNA VIBRATION
R.A.D.A.R. detects motion
Antenna vibration may cause reading
To Avoid
  Use manufacturer’s antenna mount
  Disregard readings under heavy vibration
  Use tracking history

## Slide 70: AUDIO EFFECT
R.A.D.A.R. detects motion; loud noises may cause antenna vibration
Requires a harmonic of R.A.D.A.R. frequency
To Avoid
  Do not allow loud noises around antenna
  Use tracking history

## Slide 71: MULTIPATH SIGNAL
Barely encountered phenomena
Multiple reflections each cause increase in Doppler frequency
Very high Doppler audio tone
To Avoid
  Pay close attention to audio Doppler
  Use tracking history

## Slide 72: AUTO-GAIN CIRCUITS
Automatic increase of receiver sensitivity
May cause “ghost readings”
Usually replaced by valid reading when target is processed
To Avoid
  Use tracking history

## Slide 73: OPERATIONAL RANGE CONTROL
Allows operator to control operational range of the device
Adjusts sensitivity of R.A.D.A.R. receiver to the strength of the reflected signal
Does not affect strength of the transmitted R.A.D.A.R. beam

## Slide 74: TEMPERATURE EXTREMES
Heat affects electronic, mechanical devices
May cause frequency drift, temporary R.A.D.A.R. failure
To Avoid
  Maintain an even temperature
  Discontinue use if unit gets excessively hot or cold

## Slide 75: WEATHER EFFECTS
WILL reduce R.A.D.A.R. range due to refraction
WILL NOT affect accuracy
To Avoid
  Discontinue R.A.D.A.R. use during adverse weather

## Slide 76: AUTOMATIC LOCK, AUTOMATIC ALARM
NOT ALLOWED IN NEW R.A.D.A.R. UNITS
Should be deactivated in older units
To avoid
  DO NOT USE AUTOMATIC LOCK OR ALARM

## Slide 77: JAMMING DEVICES
Presence of a R.A.D.A.R. jammer is recognizable:
  Doppler audio may be uneven and inconsistent
  If the R.A.D.A.R. device has a “transmission hold” feature, the device may receive a signal and display a speed while the “hold” feature is activated

## Slide 78: SET UP
Chapter 5

## Slide 79: R.A.D.A.R.
THREE COMPONENTS
Antenna
Box (counting unit)
Current (power source)
Connected in this order

## Slide 80: HANDHELD
Notes: Needs updated graphics

## Slide 81: VEHICLE MOUNTED
Antenna
Box
Current
Notes: Needs updated graphics

## Slide 82: VEHICLE MOUNTED
Setup of Components
Do not twist antenna and power cables together
Follow A-B-C, making sure that power is turned on LAST
Mount component securely

## Slide 83: ANTENNA MOUNTING
Security is primary objective
Use the provided brackets
Don’t intertwine power and antenna cables
Avoid use of Velcro

## Slide 84: QUESTIONS ABOUT POTENTIAL R.A.D.A.R. RISKS
To minimize potential risks:
Use good judgement
Properly maintain device
Do not aim at any part of body
Use only CPL-approved devices
Only trained operators should handle devices
Place in “OFF” or “Standby” mode when not actively in use
Contact manufacturer if you have questions about potential concerns

## Slide 85: TESTING
Chapter 6

## Slide 86: LIGHT TEST
All display indicators, lamps, etc. are tested
Usually display “8” (causes all seven segments to operate)
All must function correctly
IF NOT, REMOVE FROM SERVICE UNTIL REPAIRED.

## Slide 87: INTERNAL TESTING
Test ONLY - Not “calibration”
Procedure must follow manufacturer’s Manual of Operation
Most devices use similar testing sequence
Notes: Use LITS when setting up your device. Light Segment Test, Internal Circuit Test, Tuning Fork Test, and Speedometer Verification. This is not in every user manual, but if you follow this, your equipment should be accurate.

## Slide 88: EXTERNAL TESTING
Tuning Fork used for test
Hold in proper position relative to antenna
R.A.D.A.R. must read out to +1 mph of tuning fork’s certified speed

## Slide 89
1-2”

## Slide 90: LEGAL CONSIDERATIONS
Chapter 7

## Slide 91: JUDICIAL NOTICE
The court may accept or recognize the existence and truth of certain facts without production of evidence

## Slide 92: STATE V. DANTONIO
(June 20, 1955) 18 NJ 570, 115 A3d 35, ALR2d 460
New Jersey stationary R.A.D.A.R. case
Judicial notice taken of the Doppler principle

## Slide 93: ROYALS V. COMMONWEALTH
(March 11, 1957) 198 Va. 876, 96 S.E.2d 812
Virginia stationary R.A.D.A.R. case
Tests for accuracy at each location R.A.D.A.R. is used
Represented extreme precautionary testing

## Slide 94: THOMAS V. CITY OF NORFOLK
(April 25, 1966) 207 Va. 12, 147 S.E.2d 727
Virginia stationary R.A.D.A.R. case
Relaxed criteria for testing
Tests for accuracy at beginning and end of duty shift

## Slide 95: STATE V. TOMANELLI
(February 1, 1966) 152 Conn 365, 216 A2d 625
Connecticut stationary R.A.D.A.R. case
Use of tuning fork established as testing R.A.D.A.R.’s operation

## Slide 96: HONEYCUTT V. COMMONWEALTH
(November 4, 1966) 408 SW2d 421
Kentucky stationary R.A.D.A.R. case
Judicial notice that properly constructed R.A.D.A.R. device is capable of accurately measuring speed
No judicial notice of particular R.A.D.A.R. model
Proper training of operator required
Technical understanding not required

## Slide 97: STATE V. HANSON
(October 3, 1978) 85 Wis.2d 233270 N.W.2d 212
Wisconsin Moving R.A.D.A.R. Case
Ruled that judicial notice of particular model was improper, and five standards must be met:
  Operator adequately trained & experienced
  R.A.D.A.R. in proper working order, checked by tuning forks before & after alleged violation
  R.A.D.A.R. used in area of minimum interference
  Patrol speed display must be verified against vehicle speedometer
  R.A.D.A.R. to be externally tested within reasonable proximity of arrest (tuning forks)

## Slide 98: PROVING THE SPEED LAW VIOLATION IN COURT
Each and every specific element of the charged offense must be established
Core Elements of Proof
  Driver
  Vehicle
  Time
  Venue

## Slide 99: STAFFORD V. KARMANN
(April 28, 1978) 2 Kan.App.2d 248, 577 P.2d 836
Kansas law
An operator’s testimony is admissible as “lay opinion” even if he/she cannot be considered an expert in the field, upon a proper showing of foundation

## Slide 100: SUMMARY AND SECTION REVIEW