## Slide 1: INTRODUCTION/HISTORY
Chapter 1
Notes: LASAR and L.I.D.A.R. may be used interchangeably

## Slide 2: MODULE CONTENT
Chapter 1: Introduction and History
Chapter 2: Scientific Principles
Chapter 3: Function
Chapter 4: L.I.D.A.R. Effects
Chapter 5: Set up
Chapter 6: Testing
Chapter 7: Legal Considerations

## Slide 3: L.I.D.A.R.
ght
etection
nd
anging

## Slide 4: L.A.S.E.R.
ight
mplification by
timulated
mission of
adiation

## Slide 5: TYPES OF L.A.S.E.R.
Semiconductor
Gas
Chemical
Excimer
Free Electron

## Slide 6: HISTORY OF L.A.S.E.R.S
1989
1960
1957
1954
1939
1928
1917
Albert Einstein published paper On the Quantum Theory of Radiation
Rudolph Ladenburg proved Einstein’s theory by confirming stimulated emission and negative absorption
Valentin Fabrikant predicted use of stimulated emission to amplify light
Charles Towns, James Gordon, Herbert Zeigelk, developed MASER, microwave amplifier using stimulated emission
Gordon Gould designed the first L.A.S.E.R. on paper
Theodore Maiman built first working L.A.S.E.R.
First Traffic
L.I.D.A.R. Developed
Notes: In 1917 Albert Einstein, in his paper On the Quantum Theory of Radiation, laid the foundation for the invention of the L.A.S.E.R. and its predecessor, the maser, by introducing the concepts of probability coefficients (later to be termed 'Einstein coefficients') for the absorption, spontaneous emission, and stimulated emission of electromagnetic radiation. The paper proposed the phenomenon of stimulated emission, the basis for the LASAR
http://people.cas.uab.edu/~mirov/Lectures%201-2%20ch1%20fall%202015.pdf
http://people.seas.harvard.edu/~jones/cscie129/nu_lectures/lecture6/hertz/Hertz_exp.html
http://www.acs.psu.edu/drussell/Demos/doppler/doppler.html
https://micro.magnet.fsu.edu/optics/timeline/people/doppler.html

## Slide 7: SCIENTIFIC PRINCIPLES
Chapter 2

## Slide 8: DOPPLER PRINCIPLE
Based upon sound waves
Later determined to apply to other types of waves
“The frequency of a wave is relative to the motion between the source and the observer.”

## Slide 9
Higher Frequency
Lower Frequency

## Slide 10: RELATIVE MOTION
Stationary
Objects Moving Away
Objects Moving Towards
Notes: Needs updated graphics

## Slide 11: L.I.D.A.R. USES LIGHT WAVES
Doppler principle (based on sound) also applies to:
Light Waves
Radio Waves

## Slide 12: WAVE AND WAVELENGTH
A
Valley
A to B = WAVELENGTH
One Wave
Peak
B

## Slide 13: TYPES OF WAVES & THEIR MEDIUMS
Ripple in pond, ocean waves: Water
Sound waves, blast waves: Air
  Seismic waves (sound waves that travel through rock)
Electromagnetic waves: Space

## Slide 14: THE ELECTROMAGNETIC SPECTRUM
L.I.D.A.R. (330 THz)
X Band R.A.D.A.R. K Band R.A.D.A.R. Ka Band R.A.D.A.R.
(10.525 GHz) (24.15 GHz) (33.4 GHz-36 GHz)
FREQUENCY INCREASE (CYCLES PER SECOND)
WAVELENGTHS DECREASE

## Slide 15: WAVELENGTH
The distance in which a periodic wave repeats itself
L.I.D.A.R. wavelength ≈ 904 to 905 nm
(Nanometer = Billionth of a Meter)

## Slide 16: FREQUENCIES
Ka-Band
24.150 GHz
R.A.D.A.R.
K-Band
34.5 GHz
R.A.D.A.R.
10.525 GHz
R.A.D.A.R.
X-Band
330 THz (terahertz)
L.I.D.A.R.

## Slide 17: PROPERTIES OF LIGHT
Reflected
Metal
Concrete
Refracted
Glass
Absorbed
Grass
Earth
Sand

## Slide 18: FUNCTION
Chapter 3

## Slide 19: L.A.S.E.R.
ight
mplification by
timulated
mission of
adiation

## Slide 20: CREATING L.A.S.E.R. LIGHT
Mirror
Light
Mirror
LIGHT AMPLIFICATION by STIMULATED EMISSION of RADIATION

## Slide 21: OPTICAL RESONATOR
Lazing Medium

## Slide 22: LASING MEDIUM
Crystals
Gases
Diodes

## Slide 23: CONSISTENT PROPERTIES OF L.A.S.E.R.S TODAY
Limited divergence
  Spreads slowly
Narrow spectrum
  Occupies small portion of electromagnetic spectrum
High intensity
  Heat or brightness

## Slide 24: HOW L.A.S.E.R.S MEASURE DISTANCE
L.A.S.E.R. pulse travels from device
Reflects off target
Returns to the device
Knowing total time it takes pulse to travel can provide distance to object

## Slide 25: SPEED OF LIGHT
186,282 miles per second
Convert to feet per second:
186,000 miles/second
X 5280 feet in a mile
982,000,000 feet/second
Speed of light =
  186,282 miles per second
  1 billion feet per second
  1 foot every billionth of a second
  1 FOOT EVERY NANO-SECOND

## Slide 26: CHARACTERISTICS OF L.A.S.E.R. PULSES
Speed of a L.A.S.E.R. pulse is constant (speed of light)
Pulse width: duration / period of L.A.S.E.R. light pulse
Pulse repetition rate: number of pulses per second of transmission
  Usually 100 to 300 pulses per second

## Slide 27: HOW L.A.S.E.R.S MEASURE DISTANCE
Notes: Recall the basic formula for a time/distance calculations is:
Through algebra we can change this formula to find a distance if time and speed is known.

## Slide 28: HOW L.A.S.E.R.S MEASURE DISTANCE
A L.A.S.E.R. pulse travels to target in 125 ns
The round trip time is 250 ns
The L.A.S.E.R. divides 250 ns in half to find time it took pulse to reach target
Example 1:
L.A.S.E.R. pulse travels back to L.A.S.E.R. in 125 ns
The L.A.S.E.R. reads this as 125 ft

## Slide 29: HOW L.A.S.E.R.S MEASURE DISTANCE
Example 2:
A L.A.S.E.R. pulse is transmitted towards a car 600 ft away
Round trip time for the pulse is 1200 ns (600 ft to the car, and 600 ft back)
Dividing the round trip time by 2 gives the distance to the car
  1200 ns / 2 = 600 ns = 600 ft

## Slide 30: L.I.D.A.R.
ght
etection
nd
anging

## Slide 31: PROPERTIES OF L.I.D.A.R.S
Use gallium arsenide diodes
  904 nm wavelength
Transmits beam for short time interval
  L.A.S.E.R. pulse
Time of L.A.S.E.R. pulse
  expressed in nanoseconds (ns)

## Slide 32: BASIC L.I.D.A.R. COMPONENTS
L.A.S.E.R.
Diode
Beam Splitter
Timer / Computer
On
Off
Beam Splitter
Object

## Slide 33: TIME OF FLIGHT
R.A.D.A.R.s use the change in frequency of a radio wave
  The Doppler principle
L.I.D.A.R.s measure distance change over time
Measurement of the time is called Time of Flight

## Slide 34: HOW L.I.D.A.R.S MEASURE SPEED
L.I.D.A.R.s take several distance readings over an interval of time
A target with relative motion will provide the L.I.D.A.R. with a new distance on each pulse
The L.I.D.A.R. calculates the change in distance over change in time: s = d / t

## Slide 35: HOW L.I.D.A.R.S MEASURE SPEED
L.I.D.A.R.s can differentiate one pulse from another
Light travels very fast (one foot every 1 billionth of a second)
Time interval of pulses is very slow (approximately 300 pulses per second)
Notes: If a L.I.D.A.R. fires 300 pulses per second, then for a returning pulse to meet a departing pulse, the round trip time for the returning pulse would be 3.3 million nano seconds or 3.3 million feet – approximately 631 miles!!!

## Slide 36: HOW L.I.D.A.R.S MEASURE SPEED
Example 3:
Given target moving in relation to the L.I.D.A.R.
First pulse positions target at 400 feet
Pulse travels 800 ns round trip to target
L.I.D.A.R. divides 800 by 2 to get 400 ns:
400 ns = 400 feet
Second pulse positions target at 378 feet after 1/3 of a second
  400 ft − 378 = 22 ft per 1/3 second
  Speed = 66 ft/s or 45 mph
Notes: CLICK ON LAST LINE FOR LINK.

## Slide 37: HOW L.I.D.A.R.S MEASURE SPEED
Example 4:
1st target position – 900 ns
2nd target position – 922 ns
Time Interval – 1/3 s
Target Speed
Target Distance
Target Direction of Travel
45 MPH
922 Feet
Away

## Slide 38: L.I.D.A.R. Beam Width
0 ft
500 ft
1000 ft
18 in
36 in
L.I.D.A.R.

## Slide 39: BEAM WIDTHS
X – BAND
317 ft.
K – BAND
210 ft.
KA – BAND
157 ft.
L.A.S.E.R.
36 in.
0 ft
500 ft
1000 ft

## Slide 40: AVERAGE OF LEAST SQUARES
What if 1st pulse hits the windshield and 2nd pulse hits the grill?
An erroneous 4 feet gets added and would increase the violator's speed.

## Slide 41: AVERAGE OF LEAST SQUARES
A process used to eliminate errors
  Each pulse is mathematically plotted
  Each new plot is compared with previous data

## Slide 42: AVERAGE OF LEAST SQUARES
Distance
Time
Vehicle Approaching
Allowed limits of data
Notes: Vehicle approaching is showing a shorter time for the pulse return. Vehicle coming at you, L.I.D.A.R. firing p

## Slide 43: AVERAGE OF LEAST SQUARES
Sudden changes in targeting points can result in an erroneous speed display
This data would fall outside the limits set by the L.I.D.A.R.
Speed reading not displayed during time data falls outside limits

## Slide 44: AVERAGE OF LEAST SQUARES
Reflection from
Windshield
Reflection
From grill
Distance
Time
Vehicle Approaching

## Slide 45: AVERAGE OF LEAST SQUARES
Distance
Time
Vehicle approaching
Trapped and deleted
Data
Notes: Average of least

## Slide 46: L.I.D.A.R. TARGETING
Reflective surfaces
Color
Cleanliness
Distance
Texture

## Slide 47: AIMING POINTS ON VEHICLE

## Slide 48: L.I.D.A.R. TRACKING HISTORY
VISUAL OBSERVATION
  Target Identification
  Speed Estimation
  Target Range
  Check Environment
AUDIO CONFIRMATION
  Varies with device
UNIT CONFIRMATION
  Consistent with visual estimate
  Steady reading

## Slide 49: L.I.D.A.R. EFFECTS
Chapter 4

## Slide 50: FACTORS AFFECTING L.I.D.A.R.
Radio Frequency Interference (R.F.I.)
Random R.F.I.
Law Enforcement Radio R.F.I.
Light Devices R.F.I.
Electrical Lines R.F.I.

## Slide 51: FACTORS AFFECTING L.I.D.A.R.
Windshield
Weather
Low Voltage
Sweep Effect
Cosine Effect

## Slide 52: SWEEP EFFECT
Caused by changing targeting point while transmitting L.A.S.E.R. pulses
Creates gradual change in speed data instead of sudden change
L.I.D.A.R. may allow data in and see the change as an increase in speed depending on how wide the limits are set in the average of least squares error trappings

## Slide 53: SWEEP EFFECT
True target speed
Change in target speed due to movement of L.I.D.A.R.
Distance
Time

## Slide 54: SWEEP EFFECT

## Slide 55: SWEEP EFFECT
Vehicle Moving
May produce momentary speed reading higher than actual speed!

## Slide 56: STATIONARY COSINE EFFECT
0
35
46
49
True Target Speed = 50 mph
22
Cosine of 22 = .92
50 mph x .92 = 46.3 mph
True Speed = 50 mph
Indicated Speed = 46 mph
°
°

## Slide 57: COSINE EFFECT
Angle Degrees | 30 mph | 40 mph | 50 mph | 55 mph | 60 mph | 70 mph
0 | 30.00 | 40.00 | 50.00 | 55.00 | 60.00 | 70.00
1 | 29.99 | 39.99 | 49.99 | 54.99 | 59.99 | 69.99
3 | 29.96 | 39.94 | 49.93 | 54.92 | 59.92 | 69.90
5 | 29.89 | 39.85 | 49.81 | 54.79 | 59.77 | 69.73
10 | 29.54 | 39.39 | 49.24 | 54.16 | 59.09 | 68.94
15 | 28.98 | 38.64 | 48.30 | 53.12 | 57.94 | 67.61
20 | 28.19 | 37.59 | 46.99 | 51.68 | 56.38 | 65.78
30 | 25.98 | 34.64 | 43.30 | 47.63 | 51.96 | 60.62
45 | 21.21 | 28.28 | 35.36 | 38.89 | 42.43 | 49.50
60 | 15.00 | 20.00 | 25.00 | 27.50 | 30.00 | 35.00
90 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
True Speed as Affected by the Cosine Effect

## Slide 58: L.I.D.A.R. JAMMER
Presence of L.I.D.A.R. jammer may be recognizable when:
  Operating range is reduced
  Error code displayed
  No speed displayed

## Slide 59: SET UP
Chapter 5

## Slide 60: L.I.D.A.R. OPERATIONAL CONSIDERATIONS
Pre-Operational
Visual inspection of instrument
Transportation considerations
Function check of instrument

## Slide 61: TESTING
Chapter 6

## Slide 62: LIGHT TEST
Ensures individual light segments and indicators are functioning properly

## Slide 63: INTERAL TESTING
Internal Circuit Check

## Slide 64: EXTERNAL TESTING
Sight Alignment
Range
Delta Distance

## Slide 65: L.I.D.A.R. HEALTH CONCERNS
Safe for human exposure
Never stare directly into device lens
Never stare directly into device lens within 50 feet of device using binoculars, telescope, or other optical gain devices

## Slide 66: LEGAL CONSIDERATION
Chapter 7

## Slide 67: FUNDAMENTAL CASE LAW AFFECTING L.I.D.A.R.
Evidence must be ruled admissible
Sufficient reason to believe evidence is valid
Question concerning validity of L.I.D.A.R.:
  Is the measurement an accurate representation of the vehicle speed driven by the accused at the time of alleged violation?

## Slide 68: WHAT IMPACTS ACCEPTANCE OF L.I.D.A.R.
Do we know that the operating principles of L.I.D.A.R. are valid?
Do we know that the L.I.D.A.R. device was working properly at the time of the alleged violation?
Do we know that the operator has the necessary qualifications and performed properly at the time of the alleged violation?
Do we know that the speed measurement came from the vehicle driven by the accused?

## Slide 69: HONEYCUTT V. COMMONWEALTH
Kentucky stationary R.A.D.A.R. case
Addressed operator qualifications
  Operator not required to explain internal workings of the device
  Knowledge of scientific principle irrelevant to operation of a speed measurement device
Established that operator will have made visual estimate of target vehicle speed

## Slide 70: LESSONS LEARNED
L.I.D.A.R. Challenges and Discovery
  A 2008 case in New Jersey based on a L.I.D.A.R. citation, resulted in the conviction being reversed and remanded based on failure to comply with the following:
  Providing copies of both sides of the citation and any notes made regarding the stop
  A description of the speed-measuring device, make and model
  The officer’s training history on the R.A.D.A.R. device; where he was trained and by whom; and manufacturer’s manuals for the device
  Training manuals for the State of New Jersey and operating procedure for the speed-measuring device
  Officer‘s log showing what citations were issued that day
  Repair history of the speed-measuring device for the last 12 months
  Any engineering and speed study used to set the speed limit.
  State v. Green,417 N.J. Super.190th , 9A.3d 172, 2010 N.J. Super. LEXIS 213 (App.Div.2010)

## Slide 71: IMPACT OF NEW PRODUCTS
L.I.D.A.R. is accepted in most courts and will be received by judicial notice
When a new product is used, a Court can be demanding
  State v. Sweat, 2016-Ohio
On appeal, the court defined the requirements for acceptance of a new device, and noted they had not been met
State specific requirements are important in case preparation
State v. Sweat, 2016-Ohio-2680 *, 2016 Ohio App. LEXIS 1548 (Ohio Ct. App., Butler County Apr. 25, 2016)
State v. Helke, 2015-Ohio-4402, 46 N.E.3d 188, 2015 Ohio App. LEXIS 4267 (Ohio Ct. App., Montgomery County 2015)

## Slide 72: PEOPLE V. DE PASS (1995)
Challenged proper use of L.I.D.A.R.
Court identified proper officer training and before and after testing

## Slide 73: HAWAII V. ABIYE ASSAYE (2009)
Defendant cited for 90 mph in a 55 mph zone based on L.I.D.A.R. device measurement
Insufficient foundation was laid to admit the measurement based on:
  Officer’s training did not meet manufacturer’s requirements, even thought the officer was trained in L.I.D.A.R. operation
  With no other evidence to support the defendant’s speed; there was no way to support a conviction

## Slide 74: MEETING THE NEEDS FOR JUDICIAL NOTICE
Ensure officer’s training is well documented and meets all State or local requirements
Ensure all training requirements and standards for a particular device are met and can be demonstrated
Maintain the operator’s manual for the device in an appropriate format for easy reference and confirmation of information
Review and assess potential for challenges to new devices with appropriate authority, e.g. prosecutor’s office, court
Ensure all documentation is available, including maintenance records for each speed-measuring device

## Slide 75: SUMMARY AND SECTION REVIEW