## Slide 1: EV / HEV Safety
NISSAN MOTOR CO., LTD

## Slide 2
1. LEAF Overview
2. Lithium Battery Development at Nissan
3. Lithium Battery System Design and Safety
Agenda
Notes: 2

## Slide 3
1. LEAF Overview
2. Lithium Battery Development at Nissan
3. Lithium Battery System Design and Safety
Agenda
Notes: 3

## Slide 4
Dimensions | 4,450mm X 1,770mm X 1,545mm
Seating Capacity | 5 passengers
Powertrain layout | Front motor, front drive
Electric Motor | High response AC synchronizing motor (80kw, 280Nm)
Battery | Laminate-type thin lithium-ion battery (approximately 24kWh)
Brakes | Regenerative braking, mechanical disk brakes
Top speed | Over 140km/h
Cruising range | 160km （@ US LA4 mode）
Charging times | Normal charge: JPN approximately 8 hours(200V) US/EUR approximately 7 hours(240V/230V) Quick charge: Approximately 30minutes (@50kW SOC0% to 80%)
Specifications
Launched Dec. 2010 in JP, US, EU
Nissan LEAF

## Slide 5
Maximum torque | 280 Nm
Maximum power | 80 kW
Top Motor speed | 10,390 rpm
Motor weight | 58 kg
Motor Specifications
Dimensions | 304 × 256.5 × 144.5mm
Weight | 16.8kg
Max. AC Current (Coolant temp. : 65℃) | 425 A RMS (4 sec)
 | 340 A RMS
DC Voltage | 240 - 403V
Carrier Frequency | 5kHz
Inverter Specifications
LEAF Powertrain

## Slide 6
Chassis
Battery pack
Module
Cell
Battery Management System
Junction Box
Service Disconnect Switch Etc
48 modules / vehicle
192 cells / vehicle
4 cells / module
LEAF Vehicle Structure
Battery

## Slide 7
Cell
Module
Pack
Cell | Structure | Laminated type
 | Capacity | 33Ah
 | Cathode | Original blended (LMO based)
 | Anode | Graphite
Module | Consist of Cell numbers | 4 cells
 | Cell connection | 2 parallel-2series
Pack | Consist of Module numbers | 48 Modules (in series)
 | Total Energy | 24 kWh
 | Max. Power | >90kW
 | Power/Energy ratio | ≒4
LEAF Battery Specifications

## Slide 8
1. LEAF Overview
2. Lithium Battery Development at Nissan
3. Lithium Battery System Design and Safety
Agenda
Notes: 8

## Slide 9
In 1992, R&D began on lithium batteries for automobile applications.
Lithium
Battery
Vehicle
‘91 The world’s first LB
(for cellular phone)
’92 Research start
Co type
Mn type
Cylindrical cell
Laminated cell
‘07 AESC founded
Prairie EV
Altra EV
Hyper Mini
EV
HEV / FCV
Tino HEV
03 FCV
05 FCV
1991
2010
2000
FUGA Hybrid
LEAF
Nissan Li Battery History
Notes: We started Lithium battery research in 1992, beginning with a cobalt type battery in a cylindrical cell package.
In the late 90’s, we started developing a Mn-type cell and in the early 2000’s developed a laminated cell. This led to the current cell configuration.

## Slide 10
Long life
High energy performance
(light weight and compact)
Low cost
Reliability
Highly balanced total performance
The original blended compound cathode (LMO based)
    compatibility of low-cost and durability.
Laminated-type cell structure
    simplifying the terminal design for power-use
    improving the thermal radiation performance.
Cell designed by AESC
AESC( Automotive Energy Supply Corporation)
Cell Design

## Slide 11
High Reliability
Twice the Energy
Conventional
Laminated
Twice the Power
Compact &
Flexible Packaging
Laminated
Cylindrical
140Wh/kg*
> 2.5kW/kg*
½ the Size
Stable Spinal Mn-type crystal structure
Laminate structure provides higher cooling efficiency
Stable performance through cell control
Charge
Discharge
Conventional
Laminated
* after durability test
* after durability test
Satisfies automotive-level performance with high reliability.
Laminated Li-Ion Battery
Notes: 11

## Slide 12
How are thermal issues during extreme conditions addressed in the design of the cells and battery packs?
  Currently using Mn type Li-ion battery
  By using stable crystal structure (spinel Mn-type as electrode material) the battery can hold stability even under high heat
Manganese Oxide Lithium
Mn Oxide
Li-Ion
Metal Oxide
Li-Ion
Spinel Structure
Layered Structure
Other Metal Oxide Lithium
Discharge
Charge
Discharge
Charge
Stable
Thermal – Stable Material
Notes: 12

## Slide 13
Cylindrical Cell Battery
Laminated Cell Battery
This cell design provides higher cooling performance
Thermal – Heat Rejection
Notes: 13

## Slide 14
1. LEAF Overview
2. Lithium Battery Development at Nissan
3. Lithium Battery System Design and Safety
Agenda
Notes: 14

## Slide 15
Cell
Module
Pack
Vehicle
Electrical
Mechanical
Thermal
Potential hazardous
events
Standards
Regulations
ECE R100
IEC/ISO
SAE
UN §38.3
JIS C8714
Safety Shield Concept
Applied
Protection design
Resistance design
QC/T743
FMVSS
Vehicle, battery pack and modules are designed to act as ‘barriers’ to potentially harmful events
Apply global regulations and standards
Battery Safety Design Concept

## Slide 16
Long life
High energy performance
(light weight and compact)
Low cost
Safety/Reliability
Highly balanced total performance
Mechanical cell support
Thermal management
Waterproof
Insulation
Lay-out versatility etc.
Module/Pack Design

## Slide 17
Battery case is made from steel to create a sealed structure
Pack uses a robust interior of metal fixtures to secure components; this helps maintain the pack structure in case of accident or fire.
LEAF Battery Structure

## Slide 18
test time: 1 hour
No leak into the Pack
Immersion

## Slide 19
The LEAF battery management system performs continuous self diagnostics by monitoring:
  Individual cell voltage
  State of charge
  Battery temperature
  Battery pack hardware conditions
BMS optimizes conditions to provide power on demand
BMS responds to unexpected conditions by going to failsafe mode or complete shut down depending on the circumstances; examples:
  Overcharging
  Over-temp
  Cell failure
  Crash
Battery Management System

## Slide 20
High voltage circuit is initially open and activated only when control system is correct
Main RLY is cut off when detecting vehicle crash
Motor
Inverter
Charge RLY
Bat Main RLY
Quick charger
Q/Charge RLY
Bat Main RLY
Vehicle control module (VCM)
BMS
Check each (96 cells) voltage
and total voltage
Request RLY CUT
Cut off Main RLY
A/B sensor
Request
RLY CUT
Normal Open RLY
Input
AC
Input
AC
A
Battery pack
On board charger
SD/SW
J/B
High Voltage Circuit Diagram

## Slide 21
Impact safety concepts
ICE
EV
Passenger Protection
Body deformation control
Optimization of restraint systems
Prevention of secondary accident
Protection of fuel system
Prevention of secondary accident
Protection of high voltage system
Triple Protection Structure
Triple Electric Safety System
EV Safety
Notes: 21

## Slide 22
Triple electric safety system
Prevent high-voltage electric leakage with fuses in battery
3
Battery pack
Cut off high voltage with impact detection system
2
Cabin is structurally separated from high-voltage electric system with EV dedicated body and optimized layout
1
EV Safety
Notes: 22

## Slide 23
Triple protection structure
Battery pack
Battery module
1st Protection Structure
Suppress body deforming with impact energy absorbing vehicle body
1
2nd Protection Structure
Protect battery pack with body skeleton
2
3rd Protection Structure
Protect battery modules with
high-strength battery frame
3
1
EV Crash Safety
Notes: 23

## Slide 24
EV is tested according to the regulatory and non-regulatory requirements for all markets where it is sold
  Example: 40 mph offset frontal impact
  No damage to battery pack
EV Crash Safety
Notes: 24

## Slide 25
Cold area Test
Water-covered road Test
Uneven road Test
High pressure washers Test
Safety is evaluated by testing under a variety of situations and environments
EV Safety
Notes: 25

## Slide 26
Thank You
Notes: 26